## Slide 1
ECU HARNESS AND ENGINE HARNESS FAILURE

## Slide 2
EFFECTS OF FAILED ENGINE OR ECU HARNESS
Biggest effect of engine harness failure is ECU failure.
Sensor failure.
FIRE incidents.
Breakdown of ST, Low Pick-up, mis-firing.
Driver complaints of ST, Low Pick-up, mis-firing.

## Slide 3
BEFORE ECU HARNESS
BEFORE ECU HARNESS END CONNECTOR
Loosed harness
Hanging harness
unmounted end connectors
CAUSES OF ECU HARNESS FAILURE
THE BIGGEST CAUSE OF HARNESS FAILURE IS DUE TO HARNESS FOULING WITH SHARP EDGES OF BODY NEAR TO INSTRUMENT CLUSTER.

## Slide 4
AFTER ECU HARNESS
AFTER ECU HARNESS END CONNECTOR
MAIN CAUSE OF FAILURE BEHIND ECU HARNESS IS NOW COVERED WITH COMBINATION OF PROTECTIVE SLEEVE AND SILION SEALENT
Properly mounted harness
Properly mounted end connectors

## Slide 5
ROUTING OF ENGINE HARNESS HAS CHANGED.
RATHER THAN PASSING THROUGH AIR COMPRESSOR VIA CHASSIS CROSS MEMBER AND THEN GETS CONNECTED WITH ECU HARNESS NEAR TO RADIATOR BOTTOM, NOW ITS REROUTED AND GETS DIRECTLY INSIDE INSTRUMENT CLUSTER FROM ENGINE.
THUS MAKE IT MORE SAFE FROM HEATING AND FOULING ISSUES.
ALSO ITS ECU HARNESS CONNECTED SIDE ‘CONNECTOR’ IS SAVED FROM UNNECESSARY CORROSION, DUE TO DUST AND WATER WHICH GETS IN DIRECT CONTACT DURING WASHING, RAINING AND IN RUNNING CONDITIONS.

## Slide 6
CAUSE OF FAILURE WITH ENGINE HARNESS
HARNESS FOULING WITH RADIATOR
HARNESS FOULING WITH CROSS MEMBER
HARNESS FOULING WITH AIR COMPRESSOR PIPE
HARNESS FOULING WITH GEAR LEVER
UNMOUNTED ENGINE HARNESS FOULES WITH NEARBY COMPONENTS WHICH RESULTS IN PREMATURE FAILURES DUE TO FRICTION AND CUTTING ACTION BETWEEN TWO SURFACES, MELTING OF HARNESS DUE TO EXCESSIVE HEAT OF AIR COMPRESSOR OUTLET PIPE OR EXHAUST HEAT.

## Slide 7
BEFORE ENGINE HARNESS POSITION
ENGINE HARNESS END CONNECTOR

## Slide 8
AFTER ENGINE HARNESS POSITION
ENGINE HARNESS END CONNECTOR
END CONNECTOR ARE SECURED INSIDE INSTRUMENT CLUSTER THUS MAKING IT MORE SAFE FROM HEAT, DUST AND RAIN WATER.

## Slide 9
MODIFIED HARNESS MOUNTED BRACKETS
NEWLY DEVELOPED HARNESS MOUNTED BRACKETS

## Slide 10
OLDER BRACKET IS MADE OF TWO PIECES AND ONCE ANY PIECE GETS LOOSENED, IT DAMAGES INTAKE MANIFOLD.
NEWLY MODIFIED BRACKET IS MADE OF SINGLE PIECE ONLY AND THUS, DOESN’T DAMAGE INTAKE MANIFOLD EVEN WHEN GETS LOOSED AND ALSO ALLOWS TO MOUNT ENGINE HARNESS AND ALSO MAKES CNG INJECTORS REMOVAL VERY EASY, AS REMOVAL OF WHOLE BRACKET IS NOT REQUIRED.

## Slide 11
BEFORE
AFTER
FUSE BOX HANGING, LOSSED AND EXTRA WIRES ATTACHED
FUSE BOX MOUNTED PROPERLY, ALL WIRING HARNESS MOUNTED PROPERLY AND EXTRA WIRES REMOVED

## Slide 12
BEFORE
LOOSED ECU AND MOUNTING HOLES ARE DAMAGED
AFTER
PROPERLY MOUNTED ECU WITH NEWLY DRILLED HOLES AND IS REPOSITIONED.
ALSO EXTRA EARTHING IS PROVIDED FOR MORE SAFETY TO ECU.

## Slide 13
BEFORE
AFTER
ALL WIRING HARNESS IS SORTED CAREFULLY AND ALSO TEMPORARY OR NAKED WIRES ARE REMOVED AND PROPER INSULATION AND PROTECTION IS PROVIDED TO COMPLETE INSTURMENT CLUSTER HARNESS.

## Slide 14
EXTRA EARTHING POINT IS PROVIDED AND IS CONNECTED BETWEEN ENGINE AND CHASSIS.

## Slide 15
EXTRA PROTECTION IS PROVIDED USING COMBINATION OF SILICON SEALENT AND PROTECTED SLEEVE.

## Slide 16
ALTERNATOR AND SELF STARTER HARNESS
BEFORE
AFTER